MEMORANDUM

To                                        Werkgroep Verkeerslichten Amsterdam

From	Ane Wiersma

Doorkiesnummer	7809

E-mail	a.wiersma@dro.amsterdam.nl

Datum	9 November 2006

Onderwerp                             evaluation waiting time predictor

Introduction

In the spring of 2005 four intersections have been provided with waiting-time predictors in bicycle traffic lights. Waiting-time predictors are counters indicating in seconds the time until a green light appears.

These led-counters have been placed in the yellow lens of the traffic

light. Waiting-time predictors are only possible in fixed and in some

instances semi-fixed traffic light regimes.

The predictors have been positioned at the following intersections:

109 Prins Hendrikkade - Martelaarsgracht; bicycle light 261 in front

of café Karpershoek

113 NieuwezijdsVoorburgwal - Raadhuisstraat; bicycle light 281

for cyclists on NieuwezijdsVoorburgwal continuing towards Spui

114 NieuwezijdsVoorburgwal - Paleisstraat; bicycle light 261 for cyclists on Paleisstraat continuing towards Dam

542 Weteringcircuit; bicycle light 261 for cyclists on Weteringschans continuing to Frederiksplein; bicycle light 251 for cyclists crossing diagonally on Weteringschans towards Leidseplein.

Objective of the study

The objective of placing these waiting-time predictors is:

- promote traffic safety by reduction of red light negation

- services to cyclists

The first objective has been determined by measuring red-light negation before and after placement. These measurements have been taken on the intersections 113 (direction 28), 114 (direction 26) and 542 (direction 26). In July of 2005 an initial assessment has been made (see memorandum DRO Assessment waiting-time predictor dated 14-7-2005). The result was that no reduction in red-light negation had occurred. That was mainly due to the results of Weteringcircuit. At the other two intersections a tiny reduction in red-light negation could be

Gemeente Amsterdam

Dienst Ruimtelijke Ordening

ascertained. The high red-light negation at Weteringcircuit was probably due to the fact that at this intersection the bicycle traffic lights and waiting-time predictors were not very clearly visible. It is also quite possible that the chaotic arrangement of the intersection and low traffic amounts were one of the causes of the high red-light negation. In the benchmark the situation was more or less ‘normal’.That is why a decision has been made to exclude this intersection from the assessment of the red-light negation. To increase visibility of the waiting-time predictors in particular a decision was made to locate the counter in the lower yellow light as well. This was recommended by the previous assessment and proved to be technically feasible.

Study results

In order to determine the effectiveness red-light negation counts were conducted again. The diagram represents data from November 2004 (before placement of the predictors), May 2005 (after placement of the predictors in the yellow toplight) and September 2006 (after placement of additional predictors in the lower yellow light).

Figure 1 Red-light negation cyclists Paleisstraat towards Dam, 14.00 to 16.00 hours

Gemeente Amsterdam Dienst Ruimtelijke Ordening

Figure 2 red light negation cyclists NieuwezijdsVoorburgwal towards Paleisstraat, 14.00 to 16.00

Figure 3 red light negation cyclists Paleisstraat towards Dam, 16.00 to 18.00

Gemeente Amsterdam Dienst Ruimtelijke Ordening

Figure 4 red light negation cyclists NieuwezijdsVoorburgwal towards Paleisstraat, 16.00 to 18.00

Gemeente Amsterdam Dienst Ruimtelijke Ordening

Satisfaction

In October of 2006 a satisfaction survey was conducted as well (dienst IVV.2006). Cyclists aware of the waiting-time predictors are highly positive. The predictor was rated 8.5 (on a scale of 1 to 10).

Conclusion

Keeping Weteringcircuit out of consideration, the red-light negation at the

intersections studied decreased in relation to the previous 2 measurements. The overall percentage fell in relation to the previous 2 measurements. The differences are substantial enough to warrant more or less the conclusion that the waiting-time predictor reduces red-light negation and most certainly that a second counter in the lower light has a positive effect.

Recommendation

Employ the waiting-time predictor with counter in the upper and lower traffic light as much as possible..

# Text boxes

9 november 2006 Notitie

Pagina 2 van 5

43= red-light negation percentage percentage

600

500

400

43

55

300

65

200

100

0

9-11-2004	2-6-2005	27-9-2006

# cyclists arriving during red and negating red

# cyclists arriving during red and waiting

9 november 2006 Notitie

Pagina 3 van 5

200

150

100

50

0

9-11-2004	2-6-2005	27-9-2006

55

45

33

55= red-light negation percentage

# cyclists arriving during red and negating red

# cyclists arriving during red and waiting

600

400

200

900

800

700

500

300

100

0

2-6-2005	27-9-2006

58

54

58= red-light negation percentage

# cyclists arriving during red and waiting

# cyclists arriving during red and negating red

9 november 2006 Notitie

Pagina 4 van 5

55=

red-light negation percentage

# cyclists arriving during red and negating red

# cyclists arriving during red and waiting

| 200 150 100 50 0 |  |
| --- | --- |
|  | 2-6-2005 27-9-2006 |

100

50

25

75

0

Figure 5 Overall percentage red light negation before and after percentage voor en na

62

55

45

10-11-2004 31-5-2005 3-10-2006

9 november 2006 Notitie

Pagina 5 van 5